## Slide 1: Next generation data storage
ETERNUS AF Series
technical presentation

## Slide 2: Fujitsu storage ETERNUS
One family. Infinite possibilities.
Notes: Presenting Fujitsu Storage ETERNUS: One Family that you give infinite possibilities.

## Slide 3: Fujitsu ETERNUS AF and ETERNUS DX
Economy
Entry systems
Entry systems
AF150
ETERNUS AF all-flash arrays
ETERNUS SF storage management
ETERNUS DX hybrid storage arrays
AF250
Midrange systems
AF650
Midrange systems
Enterprise scale-out
DX60
DX100
DX200
DX500
DX600
DX900
DX8900
Notes: This slide captures the entire Fujitsu ETERNUS AF S3 and ETERNUS DX S5 product families as per segments

## Slide 4: All-flash or hybrid: which way to go?
All-flash
Hybrid disk
When currently using mainly fast disks
When consolidating structured and unstructured data in one storage
Sub millisecond latency is required
Guaranteed QoS and performance optimized storage is priority
Price per capacity (flash/disk) will reach break-even within product lifecycle
Convincing savings in operations and maintenance (think TCO!)
Data reduction can eliminate price gaps short term
Balance capacity, speed and cost with SSDs and High-capacity HDs
Extreme cache and extreme cache Pools help optimize the balance of capacity, speed and cost
Budget doesn’t permit all-flash implementation
Minimal latency fluctuations are acceptable
Notes: All these enhancements in the all-flash area encourage many IT organizations to go for it in their next purchase cycle for storage. Nevertheless, they are still good reasons to consider hybrid storage. Here are some easy rules of thumb. If your current storage system is mainly equipped with fast spinning hard disks, then you should consider going for all-flash. First of all, within the lifecycle of a new system you can expect that the price per capacity will become equal between fast disks and SSDs. For data sets where deduplication makes sense, the price difference will be eliminated at once. Furthermore, all-flash storage provides a lot of savings after purchase: they need lesser data centre space, much less power, they massively reduce maintenance costs as SSDs rarely fail and finally they require much less operational efforts for performance tuning than systems with disks. From a total cost of ownership perspective, all-flash storage is already today more economical than any other storage platform. However in scenarios where you want to consolidate a lot of structured and unstructured data in one system, hybrid storage continues to demonstrate high value. You can balance capacity speed and costs by combining SSDs and slow spinning high-capacity disks in one system. To reduce the higher administration efforts related to disks, it is highly recommended to invest in automation tools to bring these efforts down.

## Slide 5: ETERNUS AF
Next generation all-flash is here!
Notes: Now let us look at ETERNUS AF in detail.

## Slide 6: Boost storage efficiency1 in a flash!
1 Compared to disk storage. UBER: Unrecoverable bit error rate
6
© Fujitsu 2023
FUJITSU-PUBLIC
10×
more IOPS
5×
better $/IOPS ratio
10×
higher density
85%
savings for power and cooling
8×
less cost for maintenance
100
times better UBER
Notes: This slide captures the numerous advantages of flash against Disk, almost every feature is improved with flash.
For most enterprise workloads acquisition cost plus operating costs of SSDs are already lower than for equivalent HDD arrays
Enterprise-grade flash storage has an UBER of 10-18; that is 100 times better than the best HDD UBER of 10-16
The average power and cooling consumption for flash-based storage ranges from 50% to 90% less per GB
Flash storage latency is 1,000x lower than HDD storage
Flash commonly averages a 6:1 data reduction rate over a variety of data, while the HDD storage rate averages closer to 2:1
Source: https://searchstorage.techtarget.com/feature/Seven-ways-flash-data-storage-beats-HDDs-for-any-workload

## Slide 7: ETERNUS AF: Made for mainstream usage of flash
Ultra low response time
SPC benchmark records
Boost with flash
Trust in flash
Optimize with flash
High IOPS density
Flash optimized cache
Snapshots
Storage mirror
Storage cluster
Transparent failover
Deduplication/compression
Automated quality of service
DC infrastructure costs
Enterprise software licenses

## Slide 8: ETERNUS AF S3: all-flash storage for all business demands
1 Maximum raw capacity depends on available SSD types | 2 Calculation based on deduplication/compression factor of five and capacities will further depend upon data patterns and applications | 8KB Rad Read (IOPS) w/o Dedup/Comp | For more detailed product specifications please refer the product datasheets.
CPU
Form Factor
Max system memory
Number of drives
Max capacity1
Management Software
4core, 2.2 GHz
2U
32 GB
2 – 24
92 TB raw
12core, 2.6 GHz
3U
1,536 GB
2 – 1,056
32,440 TB raw
162,200 TB effective2
8core, 2.2 GHz
2U
128 GB
2 – 264
8,110 TB raw
40,550 TB effective2
600k
920k
IOPS
460k
ETERNUS SF Express
All-In flash pack
AF250 S3
AF650 S3
AF150 S3
Notes: This slide compares all the speeds and feeds of our existing all-flash systems

## Slide 9: Fujitsu ETERNUS AF S3 and ETERNUS DX S5 differentiators
Seamless family architecture
Optimized for peak performance
Intelligent data management
Always available and solidly reliable
Simplified storage operations
Notes: Fujitsu ETERNUS Fujitsu ETERNUS AF S3 and ETERNUS DX S5 have unique differentiators that distinguish it from competition:
Seamless Family architecture
  Easy upgrades and investment protection
  Simple, comprehensive and unified administration via one management platform: ETERNUS SF
Optimized for peak performance:
  Ultra-fast response times with all-flash performance
  Balancing speed and cost with the flexible combination of SSDs, SAS and nearline SAS
Intelligent data management
  Hardware accelerated Dedupe and Compression
Always available and solidly reliable
  Native Replication as well as transparent Failover (Manual or automatic) between different ETERNUS AF/DX models
  Mirroring of business-critical data via ETERNUS Storage Cluster
  Seamless and efficient data migration (both online and offline)
Simplified Storage Operations
  Automated Quality of Service
  Deduplication and/or compression – but only where required
  Automated Storage Tiering
Note: The icons used in this slide will appear in subsequent slides to illustrate ETERNUS differentiators in detail.

## Slide 10: 01 Seamless family architecture

## Slide 11: Simple, comprehensive storage mgmt.
ETERNUS SF storage management software:
One system management for the entire ETERNUS portfolio …
… with simple and transparent licensing!
Choose from menu
Check status
Define action
01
02
03
ETERNUS SF Express
Bundled with ETERNUS DX entry systems for free
Snapshot functionality included
Simple upgrade by license key
ETERNUS SF
Controller-based, capacity-independent licensing
Grow data without growing costs
Transparent license options
No unplanned investments
Notes: It is also essential to use management software having intuitive features so that you benefit from operations that run efficiently over the long-term.
With the ETERNUS SF Express management software, which comes free of charge with the ETERNUS DX entry systems, Wizard support for the complete configuration can be done in just three steps.
Make your selection in the menu
Check the system status
And define an action.
Done.
Configuration assistance
Easy expansion using a specific wizards
Operational assistance
Selection of the wizard for the specific purpose
One touch backup
Troubleshooting assistance
Clear messages
Instant explanation of the troubleshooting method

## Slide 12: ETERNUS SF: performance monitoring made easy!
The SAN component performance can be visualized at a glance, to detect and understand the performance bottle-necks and keep the system running optimally
Multiple elements like volumes, CMs and ports can be displayed together to understand the performance flow
The user decides what needs to be displayed, and the layout to display it, in order to concentrate on the useful information
Interactive navigation on the time scale allows surveying and finding significant data events from a broad range to a small interval
Performance monitoring features
© Fujitsu 2023
12
FUJITSU-PUBLIC

## Slide 13: Powerful performance monitoring feature
The SAN component performance can be visualized at a glance, to detect and understand the performance bottlenecks and keep the system running optimally

## Slide 14: Powerful performance monitoring feature
Multiple elements like volumes, CMs and ports can be displayed together to understand the performance flow
Up to 6 tabs of 24 different graphs per device can be displayed, with 5 elements on each graph

## Slide 15: Powerful performance monitoring feature
The user decides what needs to be displayed, and the layout to display it, in order to concentrate on the useful information
Each tab is fully customizable, and new graphs can be added with an easy-to-use wizard
A keyword filter makes the element selection fast and simple
Name filter
Easy to use pull down menus and check boxes

## Slide 16: Powerful performance monitoring feature
Interactive navigation on the time scale allows surveying and finding significant data events from a broad range to a small interval
Changing scale from hour to day to week and back as well as interactive interval selection
Graphics can display real time1 data, with automatic display update
Zoom in on a specific interval
Change scale at will
1 30 sec. interval

## Slide 17: Advanced Copy functions
Copies all source data (Creates a copy at the time of instruction)
Copy all source data initially, then updated portions are reflected to destination
Source
Destination
Copies all source data initially, then copies only updated portions
Source
Destination
Copies only updated data
Source
Destination
Source
Destination
Updated
Copy
OPC
QuickOPC
SnapOPC/SnapOPC+
EC/REC
Entire copy
Differential copy
Differential copy of 1st generation
Differential copy of 2nd generation
Copy
OPC | Suitable for replication creation and backup operation
QuickOPC | Suitable for database systems which need shorter backup time
SnapOPC/SnapOPC+ | Suitable for backup of data on file servers
EC | Suitable to avoid conflict with high-load operation, such as copy and batch processing
REC | Suitable for backup between different devices
High-speed disk-to-disk backup
Rich choice of copy functions tailored to usage
Notes: 17
Part of the ETERNUS SF management suite is the AdvancedCopy Manager. ACM provides a variety of copy functions according to different business requirements such as snapshots, clones and copies. The AdvancedCopy function enables high-speed disk-to-disk backup.
OPC
One Point Copy copies the entire source data at a defined point in time. A clone of the data is created which additionally requires the same capacity as the source.
OPC is suitable for replication creation and backup operation.
Quick OPC
Quick OPC comes into action once an OPC session has finished and copies only updated portions of the source volume at a defined point of time (incremental backup).
SnapOPC/SnapOPC+
SnapOPC and SnapOPC+ are both snapshot technologies. Both only copy data prior to an update which is called “copy on first write”. SnapOPC are normal full snapshots that can be concurrent. SnapOPC+ are cascaded snapshots and provide multi-generation management.
Snapshots require less capacity compared to clones because they do not copy the complete source data but point to it. This advantage also means that (different to clones) snapshots are not suitable for archiving because they depend on the availability of the source data. However, especially multiple generations of snapshots offer access to older versions e. g. of unintendedly modified data.
Equivalent Copy
EC is also referred to as “local mirror”. (The copy is saved on the same ETERNUS DX.) The process starts with copying the entire source data and continues with all incremental data. While Quick OPC copies incremental data at defined points in time, EC copies incremental data the very moment it is created. This results in highest possible recovery point objectives (RPO) and recovery time objectives (RTO).
Replicated data is accessible after splitting the mirror.
Remote Equivalent Copy
REC copies entire source data in the same way as EC, but (synchronously or asynchronously) between two ETERNUS systems.
(R)EC does provide the most advanced RPO and RTO. However, it does not provide multiple generations of data. => Most business processes are supported best with a combination of different clone and snapshot technologies.

## Slide 18: Automatic selection of copy priority
Optimize copy priority according to the server load
Business server
ETERNUS DX100/DX200 DX500/DX600/ DX900/DX8900
Change the copy priority according to the workload
Low I/O load
High priority copy
Middle I/O load
High I/O load
Operation volume
Backup volume
Operation volume
Backup volume
Automatically change
Automatically change
Medium priority copy
Low priority copy
Operation volume
Backup volume
Notes: This feature can change the copy priority mode automatically according to the workload
It can be enabled for OPC, QuickOPC and EC sessions
The administrator can select a fixed priority mode by changing the EC/OPC priority setting. ”Automatic Priority” though is recommended, because that provides the best results.
This feature makes sure that the server which accesses the source volume does not suffer from low IOPS because of copy sessions running in parallel on the same volume. The priority mode for all the running sessions on that particular source volume is adjusted dynamically
Once the load on the source volume generated by the external server is low again, all running sessions are set back to high priority.
Copyright 2013 FUJITSU LIMITED
18

## Slide 19: AdvancedCopy manager enhancements
Support for deduplication compression volumes as SnapOPC+ destination
It is now possible to use deduplication compression TPV volumes as destination volumes of a SnapOPC+ snapshot copy operation, for more flexibility and efficient use of disk space.
FUJITSU-PUBLIC
Generation 1
Generation 2
SnapOPC+

## Slide 20: AdvancedCopy improvements
SnapOPC+ generation deletion
Multiple generation snapshots are now more flexible. Instead of only being able to delete the oldest session in a multi-generation SnapOPC+ snapshot, it is now possible to delete intermediary sessions for more control.
FUJITSU-PUBLIC
DX S3/S4
1st generation (oldest)
Nth generation (newest)
2nd generation
DX S5/AF S3
…
…
Only oldest session can be deleted
1st generation (oldest)
Nth generation (newest)
2nd generation
…
…
Any of the session can be deleted

## Slide 21: AdvancedCopy improvements
SnapOPC+ cascade copy
SnapOPC+ volumes can be used as a source for snapshots. This allows to take secondary backups with an efficient use of disk space and added flexibility.
FUJITSU-PUBLIC
DX S3/S4
DX S5/AF S3
SnapOPC+
SnapOPC+
SnapOPC+
SnapOPC+

## Slide 22: Protected CLI and WEB access
Encrypted transmission by SSL/HTTPS, SSH server keys support
Encrypted transmission between ETERNUS DX and client PC.
CLI transmission encrypted by SSH.
Server certificate, SSH server keys.
FUJITSU-PUBLIC
SSL: Secure Socket Layer
SSH: Secure Shell
ETERNUS DX8900
Client PC
GUI (https)
CLI (SSH)
LAN
Notes: Regarding security, we support also HTTPS and SSH sessions. You might say, “Okay, I do not trust HTTP or Telnet” and completely disable it. In this case only encrypted connections could be setup to the management interface of the ETERNUS, like HTTPS or SSH. You can do that with so-called self-signed certificates or with certificates from a certificates authority.

## Slide 23: Fujitsu Software Infrastructure Manager (ISM)
Converged management enabling organizations to pave their path to software-defined data center
Simplified IT operations
Converged, unified management across server, ETERNUS AF/DX storage and networking using a single interface
Increased agility
Intuitive software providing actionable insights leading to reduced customer response time
Accelerate growth and innovation
Streamlined delivery of IT services to speed the transition to hybrid cloud
Upgrade from ISM Essential to ISM Advanced to take advantage of robust datacenter management capabilities.
Fujitsu Software Infrastructure Manager (ISM)
Servers
Power & cooling
Network
Cloud mgmt.
software
Storage
ISM Advanced license
ISM Essential license
Comprehensive, converged management across data center
Server management & converged
monitoring across data center
Standard version
available free of charge
Full featured advanced version
New
Notes: Fujitsu ISM is a data center management software which provides simplified and converged management across multiple data center environments including compute, storage and networking devices.
Like previous gen servers, Fujitsu ISM will also support PRIMERGY M5 servers.
The main highlight of this slide is that ISM now offers two different license options to meet different business requirements.
The ISM Advanced license which is available today is a full-featured licensed version of ISM with advanced features for comprehensive management across multiple datacenters. It also monitors 3rd party vendor devices in addition to integrating into cloud environments
ISM Essential license* on the other hand is the new free of charge version, It offers a standard version of ISM, providing essential server management functions and basic converged monitoring. The license cost is free but support is optionally available for a free. It’s available for free download from our support public site.
Customers can get started with ISM Essential license and when they need more comprehensive advanced features, they can easily upgrade using a simple license key registration.

## Slide 24: List of supported hardware for ISM v2.5
List of all supported devices listed on the support matrix
Server
Storage
Switch
PRIMERGY RX S7 and later
PRIMERGY BX S3 and later
PRIMERGY CX M1 and later
PRIMERGY TX S7 and later
PRIMEQUEST 2000
PRIMEQUEST 3000
ETERNUS DX/AF S2 and later
NetApp FAS
NetApp AFF
PSWITCH 2048
SR-X
CFX
Cisco Catalyst
Cisco Nexus
Extreme Switches
Arista
Brocade FC Switch

## Slide 25: 02 Optimized for peak performance
Notes: Fujitsu has been developing the ETERNUS portfolio for many years – without making any compromises when it comes to satisfying the highest performance and quality requirements. And that translates into high value for our customers. The ETERNUS Primary Storage Family is based on an award-winning performance architecture that delivers the fastest response times even under extreme workloads. That puts you in a good position: ETERNUS offers you the best solution for every kind of business requirement – such as ultra-fast response times with all-flash performance or the optimal balance between costs and speed through the flexible combination of SSDs, SAS and nearline SAS in one system.

## Slide 26: Faster than ever before!
AF250 S3 v/s AF250 S2
8KB Rad Read (IOPS) w/Dedup/Comp and response time be less than 1.0ms
AF650 S3 v/s AF650 S2
8KB Rad Read (IOPS) w/Dedup/Comp and response time be less than 1.0ms
×2.36
×2.04
All IOPs (Performance values/ratio) are dependent on usage scenarios
Notes: The new generation of ETERNUS AF S3 and ETERNUS DX S5 systems offer significant performance enhancement over the previous generation. This slide captures the degree of improvement in each product.

## Slide 27: The world’s best performance
The world’s best performance ETERNUS DX/AF series lead the market by attaining the world’s best performance scores
ETERNUS AF250 S2
Nov, 2017 | The best $/IOPS SPC-1 result
ETERNUS AF650
Dec, 2016 | The best midrange class SPC-1 result
ETERNUS DX80
September, 2009 | The best entry class SPC-1 result
ETERNUS DX80 S2
December, 2011 | The best entry class SPC-1 result
ETERNUS DX600 S3
July, 2014 | The best midrange class SPC-1 result
ETERNUS DX440 S2
June, 2012 | The best midrange class SPC-1 result
2019
2014
2013
2012
2011
2010
2009
2016
2017
…
…
ETERNUS DX200 S3
December, 2013 | The best entry class SPC-1 result
ETERNUS DX440
March, 2010 | The best midrange class SPC-1 result
ETERNUS DX8700 S2
December, 2012 | The best enterprise class SPC-2 result
ETERNUS DX8900 S3
May, 2016 | The best enterprise class SPC-2 result
ETERNUS DX200 S4
May, 2017 | The best entry class SPC-1 result
ETERNUS DX8900 S4
April, 2019 | World’s highest IOPS SPC-1 result
V01
Notes: This slide captures the historic record of ETERNUS AF/DX systems on SPC-1 benchmarks, Fujitsu Systems have always been at the top in most benchmarks at the time of launch.

## Slide 28: The world’s best performance
The world’s best performance ETERNUS DX/AF series lead the market by attaining the world’s best performance scores
ETERNUS AF250 S2
Nov, 2017 | The best $/IOPS SPC-1 result
ETERNUS AF650
Dec, 2016 | The best midrange class SPC-1 result
ETERNUS DX200 S3
December, 2013 | The best entry class SPC-1 result
ETERNUS DX80
September, 2009 | The best entry class SPC-1 result
ETERNUS DX440
March, 2010 | The best midrange class SPC-1 result
ETERNUS DX80 S2
December, 2011 | The best entry class SPC-1 result
ETERNUS DX600 S3
July, 2014 | The best midrange class SPC-1 result
ETERNUS DX8700 S2
December, 2012 | The best enterprise class SPC-2 result
ETERNUS DX440 S2
June, 2012 | The best midrange class SPC-1 result
ETERNUS DX8900 S3
May, 2016 | The best enterprise class SPC-2 result
ETERNUS DX200 S4
May, 2017 | The best entry class SPC-1 result
ETERNUS DX8900 S4
April, 2019 | World’s highest IOPS SPC-1 result
2019
2014
2013
2012
2011
2010
2009
…
2016
2017
…
V02
Notes: This slide captures the historic record of ETERNUS AF/DX systems on SPC-1 benchmarks, Fujitsu Systems have always been at the top in most benchmarks at the time of launch.

## Slide 29: 03 Intelligent data management
Notes: The challenges of data growth are many and varied, which is why accessing, managing, and storing data intelligently can help reduce storage costs and harness valuable data. ETERNUS Primary Storage makes use of hardware accelerated compression technology for greater data efficiency without negatively impacting performance. Offloading the compression and/or deduplication process to the Storage Acceleration Engine (SAE) results in hardware-accelerated compression/deduplication that is much faster than conventional data reduction technologies. What’s more, data reduction technologies with flexible setting options allow for the precise usage of data deduplication and compression.

## Slide 30: Enterprise-class data reduction technology: now in midrange storage
Data compression and deduplication with minimal performance impact
Offloading the compression and/or deduplication process to Storage Acceleration Engine (SAE)1 leads to
1 Available on AF250 S3, AF650 S3, DX500 S5, DX600 S5, DX900 S5 and DX8900 S4 offer compression only
2 Ratio will vary depending on customer data type
Storage acceleration engine
01
02
03
Hardware accelerated compression/deduplication which is faster than conventional compression/dedup
Data reduction up to 50%2
Leads to smaller configuration in flash environments
Notes: AF250 S3, AF650 S3, DX500 S5, DX600 S5, DX900 S5 and DX8900 S4 (Compression only) offer Enterprise-class data reduction technology in Midrange storage
Storage Acceleration Engine: CPU resource consumption is reduced offloading the compression process into Storage Acceleration Engine (SAE) by own IP, so the performance improves.
Offloading the compression and/or deduplication process to Storage Acceleration Engine (SAE) leads to
  Hardware accelerated compression/deduplication which is faster than conventional compression/dedup
  Data reduction up to 50%2
  Leads to smaller configuration in flash environments

## Slide 31: Data reduction efficiency at scale
Offloading the compression/ dedup process into Storage Acceleration Engine (SAE)
Optimal Unit of Compression (8K) for database environments
Performance boost
Data Integrity assurance
Equipped with Self diagnostic function
Improved reliability
Data compression in scale out in DX8900 S4
The compression process is distributed between all CMs (24 CMs in maximum)
Performance of the compression process improves in proportion to the number of CM
Cache mirroring is assured by SAE
Notes: Let us now go into the details of data compression used in this storage system:
Performance Boost:
  Storage Acceleration Engine: CPU resource is reduced by offloading the compression process into Storage Acceleration Engine (SAE) by own IP, so the performance improves.
  The unit of data compression is changed to 8KB. To optimize it to the database environment, the unit of the compression process was adopted for 8KB. As a result, the performance improves by making internal process efficiency.
Improved Reliability
  Data Integrity assurance: Assure compress consistency, decompress is automatically executed by parallel processing
  Cache mirroring is assured by SAE
  Equipped with Self diagnostic function.
Data Compression in scale out in DX8900 S4
  The compression process is performed among multiple CMs (24CMs in maximum). As a result, the performance of the compression process improves in proportion to the number of CM.
Features of Storage Acceleration Engine:
Multi Engine: Equipped with more than CPU core number of engines. Increases hardware resources, reduces software overhead
Compress/Decompress: Coordination with Firmware Architecture. High-load CPU processing offload to SAE
Zero data detection: Zero data is detected in parallel during compression process. No additional overhead.
On-the-fly BCC Check: BCC protection of all data passing through SAE, assure reliability without performance overhead
Data Integrity assurance: Assure compress consistency, decompress is automatically executed by parallel processing
Error Containment: Equipped with Self diagnostic function. Preventing error effect to other CM
Auto Data Transfer assurance: Cache mirroring is assured by SAE. Auto check of other CM data transfer status

## Slide 32: Data reduction: à la carte
Deduplication Compression
Compression only
Deduplication only
No data reduction
Capacity savings/performance impact
No extra license costs
1 Heavily dependent on use case
ETERNUS provides flexible data reduction options
Pool #4
Pool #2
Pool #3
Pool #1
Thin provisioning is turned on by default
Decide on application level which option provides the best results
Intelligent use of data reduction
Five times less capacity1 is needed
Keep it off for applications with performance SLAs
Thin provisioning
Notes: ETERNUS also offers you optional data reduction capabilities which can be achieved through compression and or along with deduplication
Be aware though that data reduction technologies do not suit all data types – some are already compressed, for example. Also, turning on data reduction inherently adds a degree of latency back to the storage, which may be a bad idea if absolute performance is vital.

## Slide 33: Optimized block access size for SSDs
SSD
Write without 4K alignment
SSD
Controller
Read existing page with space
Write with 4K alignment
SSD
Controller
CM1
Write request for 8KB data
… Page (4KB)
… Existing data
… New data
1 CM: Controller Module
1
2
3
4
1
Add 8KB and make three pages
2
Write to the new page
3
Change old data to invalid data
4
Split 8KB in two pages & write
1
1
Notes: Improving SSD write performance
The frequency of the garbage collection which affect the performance becomes lower
Efficient write extends SSD lifetime

## Slide 34: Automated selection of optimal Write I/O
Regular processing
AF150/250/AF650
CM#01
CM#11
System
memory
CPU
System
memory
Data cache
Parity
RAID group
SSD
SSD
SSD
SSD
SSD
Flexible Write Through processing
1 CM: Controller Module
The controller decides the target write I/O and chooses Flexible Write Through processing automatically
1
Writing from the controller to SSD at high speed is made the best use of SSD performance
2
Data cache mirroring between CMs becoming a bottleneck is not done in AF, but directly write the data and the parity into SSD
3
Question: Decision Criteria
AF150/250/AF650
CM#01
CM#11
CPU
System
memory
CPU
System
memory
RAID group
SSD
SSD
SSD
SSD
SSD
1
2
3
3
CPU
Server
Data cache
Parity
Data cache
Parity
Server
Notes:   Maximize the write IO performance with the minimum communication penalty between CMs
    The CPU load on CMs are reduced
    Sequential write performance is improved drastically

## Slide 35: Controlling write back priority during garbage collection
Server
CM1
System memory
RAID group
SSD
SSD
SSD
SSD
SSD
RAID group
SSD
SSD
SSD
SSD
SSD
CPU
1 CM: Controller Module
1
2
3
Performing garbage collection (GC) is detected on an SSD basis
1
Load to SSDs in a RAID group is equalized by giving priority to write back-end processing excluding SSDs performing GC
2
When delay of write back-end processing is detected in a RAID group, it gives priority to processing in the other RAID groups
3
Write response is improved by leveling back-end write processing
Load to CPU is reduced
Benefits
Avoid bad influence on performance in front-end processing
Notes:   Controlling write back priority to keep the quick write response time

## Slide 36: The flash diet
1 Heavily dependent on use case | 2 Calculation based on deduplication/compression factor of five
A
B
C
B
A
D
B
A
B
C
D
D
C
A
D
Deduplication
B
Reduces cost for flash & Increases life span for flash.
Flexible configuration options
Decide on application SLA (volume basis) whether to use or not
Five times less SSD capacity1 is needed
Boosting effective capacity of AF150 to 450 TB2
Boosting effective capacity of AF250 to 40,550 TB2
Boosting effective capacity of AF650 to 162,200 TB2
No extra license costs
ETERNUS AF provides “inline” deduplication/compression
Notes: MORE powerful hardware (CPU/Cache)
With data reduction the all-flash data center becomes more cost effective
Each of them -- dedup, compression and thin provisioning -- has value

## Slide 37: Inline deduplication/compression
Data writes from server to system memory
1
Performing inline (system memory) data reduction
2
Deduplicated data is compressed
3
Improve storage efficiency of SSD
Reduce amount of data writes to SSDs to extend their life span
Benefits
Only reduced amount of data is written to the pool
4
1 CM: Controller Module
CM1
System memory
A
B
C
B
A
D
C
D
B
A
B
C
D
A
B
C
D
Pool
A
B
C
D
1
2
2
4
Server
CPU

## Slide 38: Solid State Drive (SSD) support: 2.5”
Fast and power saving 2.5” drives
Capacity
400 GB
SAS-3 12 Gbit/s drive interface
960 GB
1.92 TB
3.84 TB
7.68 TB
15.36 TB
30.72TB
Self-encrypting drive
1.92 TB
3.84TB
7.68 TB
38
FUJITSU-PUBLIC
Notes: Here an overview of the 2.5” drives.
Advantage of the 2.5” drives are speed and small form factor. Smaller HDDs also means less rotating mass and thus less power consumption per drive.

## Slide 39: 04 Always available and solidly reliable
Notes: The ETERNUS Primary Storage Family supports nonstop operations very efficiently. It features best-in-class continuity management, including native replication, mirroring and transparent failover (manual or automatic). Mission-critical data is mirrored automatically in an ETERNUS Storage Cluster and can be executed in both directions and between different models or generations, as well as between all-flash and hybrid. What’s more, the high interoperability of the ETERNUS AF/DX systems enables very smooth migrations (offline and online) from an old system to a new one. For example, with the unique online storage migration, you can migrate seamlessly without interrupting ongoing operations – and from ETERNUS DX to AF models as well.

## Slide 40: Tolerance against DE failure
DE#04
DE#02
DE#01
CE
DE#03
DE#04
DE#02
DE#01
CE
DE#03
CE
DE#04
DE#01
DE#03
DE#02
DE#04
DE#02
DE#01
CE
DE#03
IOM0
IOM0
Cabling between a CM and last drive enclosure in the connection chain ensures fault tolerance
In the case of DE failure, reverse cabling allows CM to access to other expansion DEs.
Conventional cabling (cascade)
Reverse cabling
DE#03 Failure
IOM1
IOM0
IOM1
IOM0
IOM1
CM0
CM1
IOM0
IOM1
IOM0
IOM1
IOM0
IOM1
IOM0
IOM1
CM0
CM1
IOM0
IOM1
DE#03 Failure
IOM1
IOM0
IOM1
IOM0
IOM1
CM0
IOM0
IOM1
IOM0
IOM1
IOM0
IOM1
IOM0
IOM1
CM0
CM1
IOM0
IOM1
CM1
Cascade connection
(Connected to next DE)
If DE#03 fails, impossible to access DEs behind DE#03
Reverse connection
(Connected to last DE)
Access to other expansion enclosures in the chain is secured
CE: Controller Enclosure DE: Drive Enclosure
Notes: 40
Reverse cabling is a feature that was requested by a lot of customers.
In the past all the shelves were attached to each other in one sequence, like a daisy chain. There was the unlikely possibility of a shelf failure which would lead to the unavailability of all the subsequent shelves.
This danger can be eliminated with reverse cabling, because there are always two independent ways to a single shelf, one path going from bottom to top and the other path going from the top down to the bottom as shown in the left picture. In the (unlikely) event of a failure only access to the affected shelf gets lost, all the others are still accessible
A RAID design that puts each member disk of a RAID group in a different shelf will survive a shelf outage easily, and this makes the DX S4 together with this new cabling design even more powerful and stable.

## Slide 41: Self-Encrypting Drive (SED)
1 AES (Advanced Encryption Standard) is an encryption standard of the Federal Information Processing Standards
ETERNUS AF also supports controller-based (128-bit AES1) encryption
Self-encrypting drives
Non-encrypting drives
Same access speed as non-encrypting drives
Encryption settings are not re-quired when adding a new drive
ETERNUS AF Series
Notes: Self-encrypting drives (SED)
In order to ensure full data security, the ETERNUS DX family supports self-encrypting drives (SED). Self-encryption means that all the data transferred to the storage medium is automatically encrypted internally before the data is written – and vice versa. When the data is read from the storage medium, the data is automatically decrypted into plain text. All data passing the interface between the host controller and the disk drives interface is in plain text. The internal encryption process is transparent for the host. All read/write operations for the host are business as usual.
The plain text is encrypted (cipher text) when it is written to the disk and decrypted (deciphered) back to the original text when it is read from the disk. The encryption and decryption engines use the same secret internal data encryption key for this process.
Let‘s throw a glance on controller-based encryption vs. self-encrypting drives:
Controller-based encryption means, data is encrypted by controller of device. Therefore, performance of data access is inferior to that of non-encrypted data access.
The self-encrypting drive has an encryption function in itself: No load is placed on the controller, and the same performance as non-encrypted data access can be achieved.
In addition, it is unnecessary to set encryption for each data because the entire drive data is encrypted. This reduces data management time and effort.
Both methods avoid leaking information from replaced drives (e. g. during maintenance) even if they are not physically destroyed.

## Slide 42: Supported RAID levels
ETERNUS AF supports the following RAID configurations
RAID 0
RAID 1
RAID 1+0
RAID 5
RAID 5+0
RAID 6
Divides data into blocks, and writes them to multiple drives in a dispersed manner (striping)
Writes data to two drives simultaneously (mirroring)
Combination of RAID0 and RAID1 Stripes mirroring data
Writes striping data and parity data created. Distributes parity data to multiple drives. Able to recover from one drive failure in the RAID array
Stripes 2 groups of RAID5
Distributes two types of parities to different drives (double parity). Able to recover from two drive failures in the RAID array
D
C
B
A
C
A
D
B
D
C
B
A
D
C
B
A
D
C
B
A
D
C
B
A
C
A
D
B
C’
A’
D’
B’
D
C
B
A
O
K
P-EFGH
D
M
I
E
A
P-MNOP
J
F
B
N
P-IJKL
G
C
P
L
H
P-ABCD
D
C
B
A
P
K
P-GH
D
M
P-IJ
E
A
N
I
P-EF
B
O
P-KL
G
C
P-OP
L
H
P-CD
P-MN
J
F
P-AB
D
C
B
A
N
P2-IJKL
P1-EFGH
D
M
I
E
A
P1-MNOP
J
F
B
P2-MNOP
P1-IJKL
G
C
O
K
P2-EFGH
P1-ABCD
P
L
H
P2-ABCD
Notes: RAID levels that we support are still a RAID 0, RAID 1+ 0, RAID 5. Additionally RAID 5+0 is supported with a maximum configuration is 15 plus 1 plus 15 plus 1. A RAID 5+0 can hold up the maximum number of 32 disk drives in the same RAID configuration. Last thing is the RAID 6 support which is still available with a maximum of a 14 plus 2.

## Slide 43: Fast Recovery
Fast rebuilding eliminates risks of system down
Reduction on rebuilding time of disks (from 9 hours to 1.5 hours for 1TB)
Instead oft many to one, many to many is used
The capacity efficiency is 55% to 80% which is higher than that of competitors
Equivalent performance to the conventional RAID
Reserved Area
～
Parity
3
1
Disk#0
X
～
Reserved Area
Parity
2
Disk#1
Y
～
5
Reserved Area
Parity
Disk#2
Parity
～
4
Reserved Area
Disk#3
Reserved Area
Disk#n
…
Reserved Area
～
Parity
3
1
Disk#0
X
～
Parity
Y
～
5
3
Parity
Parity
～
6
4
1
Reserved Area
Disk#n
Parity
2
…
Logical volumes are divided into several sections. All HDDs contain reserved area.
(Note) Fast Recovery requires RAID6-FR Volume. Reserved Area consumes user area.
RAID6-FR
When disk failure occurs, rebuilding to reserved areas is performed at once.
Disk#2
Disk#1
Disk#3
Notes: Rebuilding your data in case of a failed drive can take a very long time. The worst case may require not even hours, but maybe days or even weeks. Vast rebuild times – in combination with growing disk capacities - were the reason to implement Fast Recovery. This feature is available for RAID 6-FR raid groups. Fast Recovery utilizes reserved area on each member disk in a RAID group, summing up to the capacity of a single disk. This means at the end of the day a RAID 6-FR, which is normally an N+2 setup, will be reduced to an n+3-like configuration. A RAID 6-FR with e. g. 8 drives will have a usable capacity of 5 drives. The bigger the RAID-group, the better the ratio between the number of drives and usable capacity. In the event of a disk failure fast rebuild shortens the rebuild time by 50% to 85%, because all disks can participate in the rebuild.
The main difference is that conventional rebuild provides a bottleneck with many to one (HS) write accesses while Fast Recovery writes on the reserved space of all disks in the RAID group (many to many).
The efficiency of usable capacity is 60% to 80% (other vendors use similar techniques, but sometimes have less than 50% usable capacity). Performance is equivalent to RAID 5, especially during rebuild.
Fast Recovery can be selected on a per raid-group level.
After initial redundancy had been restored an additional disk can be added again to also restore the initial capacity without any impact on data protection.

## Slide 44: Fast Recovery speeds up rebuild processes
© Fujitsu 2023
54 hours
Time to rebuild a hard disk with 6 TB capacity
9 hours
with conventional rebuild!
rebuilt time with Fast Recovery
Rapid disk rebuilds
Fast Recovery can rebuild a RAID group five to six times faster than typical rebuild techniques
When compared to the conventional rebuild function using spare disks only, Fast Recovery can complete the process for a 1 TB disk in just 90 minutes instead of nine hours
Fast Recovery enables enterprises to use low-cost SATA disks for their productive applications
New
6.0 TB

## Slide 45: Dynamic Hot Spare
Hot spare (HS) disk is built into RAID configuration after completion of rebuild. The replaced disk dynamically becomes HS  Copy-back is not necessary
Copy-back process
Dynamic hot spare without copy-back
DE#10
DE#00
DE#10
DE#00
HS
Warning
HS
Rebuild/Redundant Copy
Rebuild/Redundant Copy
RAID 1
RAID 1
Comple- tion
Changing RAID Configuration
Copy-back is unnecessary
Replaced Disk becomes HS
DE#10
DE#00
DE#10
DE#00
Warning
HS
RAID 1
Comple- tion
Replaced Disk
RAID 1
HS
Copy-back
© Fujitsu 2023
FUJITSU-PUBLIC
Notes: Copy-back and copy-back-less operation
Dynamic Hot Spare (DHS) is a valuable option for RAID groups different to RAID 6-FR.
As standard after replacement of a failed disk, data on the hot-spare disk is retrieved (copied back) to the new disk. The copy back function restores the RAID group while maintaining redundancy after the rebuild has been performed for the hot-spare in the RAID group.
DHS with copy-back-less function is a feature which builds hot-spare disks into a RAID configuration after completion of rebuild or redundant copy. This means different to the standard approach the (previous) hot spare remains part of the RAID group while new replaced disk is dynamically promoted as hot spare.
This feature means that the copy-back process is no longer required, the RAID group is restored sooner (with positive effects on the systems performance and data protection).

## Slide 46: Disaster Recovery: REC
Reliable operation in disaster scenarios
Remote Equivalent Copy (REC)
Avoids data loss due to human error or natural disasters
Synchronous or asynchronous mode
Replication between multiple systems classes and generations
From local range to global range
Supports FC, iSCSI and Wide Area Networks
Primary site
ETERNUS SF AdvancedCopy Manager
Source
ETERNUS AF Disk storage system
SAN
Building A
Fibre Channel switch
Destination site
ETERNUS SF AdvancedCopy Manager
Destination
ETERNUS AF Disk storage system
SAN
Building B
Fibre Channel switch
Fibre Channel 10 km
Notes: Equivalent Copy
  EC is also referred to as “local mirror”. (The clone is saved on the same ETERNUS DX.) The process starts with copying the entire source data and continues with all incremental data. While Quick OPC copies incremental data at defined points in time, EC copies incremental data the very moment it is created. This results in highest possible recovery point objectives (RPO) and recovery time objectives (RTO).
  Replicated data is accessible after splitting the mirror.
Remote Equivalent Copy
  REC copies entire source data in the same way as EC, but between two ETERNUS systems. (This could be called “remote mirror” - at least in synchronous mode).
  REC allows copying data between different ETERNUS DX systems over long distances. E. g., data from an ETERNUS DX 90 S2 in a branch office in Paris is copied to an ETERNUS DX8900 S3 in a London-based headquarter asynchronously via WAN.
  Recommendation: Round trip time in asynchronous mode should not exceed 100 ms and 10 ms in synchronous mode.
(R)EC does provide the most advanced RPO and RTO. However, it does not provide multiple generations of data. => Most business processes are supported best with a combination of different clone and snapshot technologies.
[not to be presented/spoken]
10 km FC distance in this graphic is subject to respective SFPs. Other SFPs are also available as well as the option to cascade.

## Slide 47: Data integrity with Data Block Guard
Written data
Controller module
3
2
1
Apply check code
Verify check code
Verify & delete check code
Data block guard
Avoids data corruption.
Write
Read
Cache ECC protected
Drive
1
3
2
2
CC
A0
CC
A1
CC
A2
CC
A0
CC
A1
CC
A2
A0
A1
A2
User data
CC: check code
CC
A0
CC
A1
CC
A2
A0
A1
A2
User data
ETERNUS DX disk storage system
8-byte check code is added to every 512-byte data
Notes: “Data Block Guard” adds check codes during write operations. While verifying the codes for the read/write operations, it guarantees data integrity at multiple checkpoints along the data transmission route.
Check code is added to the user data received from the server (when data is written from the server).
Data consistency of entire storage systems is checked and ensured by checking (removing) the check code when data is sent to the server (when data is read by the server).
Data Block Guard verifies data integrity even in case of physical disk errors like bad blocks or sectors.
This function is controller-based and safeguarding the complete data path within ETERNUS DX.

## Slide 48: Event notification
Events to be notified – can be set individually |  | 
Error | Needs maintenance | Incident details, abnormal temperature, low battery, etc.
Warning | Needs preventive maintenance | Correctable memory error, preventive disconnection of drive which exceeds quality threshold, etc.
Information | Device information | Power ON/OFF, firmware update, RAID creation/deletion, etc.
Event notification without management software
Supports three types of internal notification methods and notification to remote support center
Notification by e-mail are supported (new)
Sends detailed information, such as required spare part, mounting position
Reduces maintenance response/recovery times
© Fujitsu 2023
E-mail: management information
SNMP: management information
Syslog: event log
AIS connect: remote access
Mail server
SNMP server
Syslog server
E-Mail
ETERNUS AF650 S3
LAN
AIS connect
Syslog
SNMP
Remote support center
Notes: How to monitor the system? SNMP and syslog had already been available for the predecessor. ETERNUS DX support email as well – without some kind of management station in-between.
Additionally – subject to an additional service contract - ETERNUS can be monitored via AIS connect and (if agreed by the customer) remote access can be granted to technical support.

## Slide 49: Online data migration
Storage migrations can be conducted during business operations
Reduced migration time
No additional software nor licenses are required
No dedicated equipment for data migration is needed
Supported on all DX S3/AF series or later models (as source storage)
Data migration with online storage migration
Data migration in progress
Data flow during business operations
Data flow during a data migration
Destination DX900 storage system
Business server
Business server
Business server
Source ETERNUS AF250
Source ETERNUS AF250
Destination DX900 storage system
Online storage migration
Business uptime
Business uptime
Notes: The high interoperability between ETERNUS storage models and generations enables a very smooth and step-by-step migration from an older system to a new one.
The image is a pictorial representation of Online Storage Migration.
  During a data migration with offline Storage Migration, the destination storage system views and copies the data in the source storage system. Because the storage system migrates the data, the migration time can be reduced. However, as is the case with migrations via a server, business operations must be stopped during a data migration to prevent the data from being changed.
  Online Storage Migration allows the business server to read from and write to the destination storage system while data is being migrated from the source storage system. Operations can be resumed immediately after the cables are switched. Therefore, downtime can be reduced significantly with online Storage Migration.
ETERNUS Benefits
Both online Storage Migration and offline Storage Migration are supported
Without going through servers, data migration time is reduced
No additional software nor licenses is required
No need to change the configuration of the source storage system
No dedicated equipment for data migration is needed

## Slide 50: Seamless and efficient data migration
Operate
Migrate
Setup
Write command processing
Host
Destination storage
Source storage
Not migrated area
Migrated area
Write
Write
Write
Write
Data migration
Establish connectivity
Configure the new array
Link the new array with the host
Host accesses only via new array
Data migration by using RAID migration
Repeat the process for all hosts
Take out the old array
Enjoy the new functions
Benefit from the new performance

## Slide 51: Replication made easy!
Branch offices
Headquarter
ETERNUS AF150 S3
ETERNUS AF650 S2
ETERNUS DX200 S3
ETERNUS DX900 S5
WAN
Notes: Specially designed to safeguard business-critical data, ETERNUS AF/DX supports uninterrupted operations at all levels. Housing a rich set of data replication and copying features, ETERNUS AF/DX enables flexible local, central and remote data management and disaster recovery concepts – even between different system classes. All this minimizes downtime and ensures business continuity.

## Slide 52: Simplified disaster recovery1
1 Available with ETERNUS DX S3/AF or later models
2 Failover not available between DX S3/S4/AF S1/S2 and DX S5/AF S3 systems
Most flexible DR options
Replication, mirroring, failover
Between model sizes
Between generations2
Between all-flash and hybrid
Production site
Recovery site
Disaster recovery
Replication
Mirroring
Failover2
All-flash
All-flash
AF150 S3
AF250 S1/S2/S3
DX100 S3/S4/S5
DX200 S3/S4/S5
DX500 S3/S4/S5
DX600 S3/S4/S5
DX900 S5
DX8900 S3/S4
AF150 S3
AF250 S1/S2/S3
DX100 S3/S4/S5
DX200 S3/S4/S5
DX500 S3/S4/S5
DX600 S3/S4/S5
DX900 S5
DX8900 S3/S4
Hybrid
Hybrid
AF650 S1/S2/S3
AF650 S1/S2/S3
Notes: As corporate data are the most critical resource in a digital enterprise, a disaster recovery configuration of storage becomes a must. Nevertheless, the costs for disaster recovery needs to be as low as possible to have more IT budget available for innovation projects. By offering a unique flexibility in DR configurations, customers can benefit from reducing storage cost for business continuity. For instance, all-flash ETERNUS AF storage which is used in production can be backed-up by hybrid ETERNUS DX systems at a lower price.
As typically not all data are mission critical, it is also possible to invest in a smaller model for disaster recovery than for the production storage. Finally, all ETERNUS AF and DX models are compatible between different generations allowing to use a new system for production in an already existing, older system for failure situations. This is possible because data replication and mirroring as well as transparent failover can be configured between different model sizes of ETERNUS AF and DX and even between the S3 and S4 generations. These capabilities are unique in the market.

## Slide 53: Guaranteed business continuity
  ETERNUS
  systems
  Active-active cluster between
1 Available with ETERNUS DX S3/AF or later models
FUJITSU-PUBLIC
Take out the risk with ETERNUS storage cluster1
Mirroring of business-critical data
Storage cluster between
ETERNUS AF and ETERNUS DX
Non-stop operations
Transparent failover
Automated/manual
Notes: Mirroring of business critical data via ETERNUS Storage Cluster is one of the other unique features of ETERNUS:
In case of a primary storage or site failure, the secondary storage takes over identities (IDs)
Failover can be executed in both directions and between different ETERNUS AF/DX models
Automatic or manual failover

## Slide 54: Storage cluster
Transparent failover eliminates risks of outage
Volumes are mirrored by REC function
Failover can be executed in both directions and between different ETERNUS AF/DX models (except ETERNUS DX60)
Active
Standby
Business data mirror
Storage Cluster Controller
Replication suspended
© Fujitsu 2023
FUJITSU-PUBLIC
Business data
ETERNUS AF
ETERNUS AF
Monitoring
Monitoring
SAN
Outage
Business Server
Active
Standby
Business data mirror
Storage Cluster Controller
Replication suspended
Business data
ETERNUS AF
ETERNUS AF
Monitoring
Monitoring
SAN
Business Server
Notes: 54
Storage Cluster is the high-availability feature of the ETERNUS DX/AF family. Data is synchronously mirrored between two interlinked systems. In case the primary (active) storage system becomes unavailable (e. g., due to flood, earthquake or other disasters) all primary host connections are switched instantly to the secondary (standby) system. This failover is transparent for both, servers and applications and ensures uninterrupted operations.
Simplifying the picture: Storage cluster consist of Remote Equivalent Copies plus the automated failover. However, different to “normal” clusters the failover is transparent to the servers. That means, the servers do not recognize any changes and no action is required at the server side.
In case of a primary storage or site failure, the secondary storage takes over identities (IDs)
I/O is continued by the secondary ETERNUX system transparently
Failover can be executed in both directions and between different disk and flash models
Automatic or manual failover

## Slide 55: TFO groups/capacity for Storage Cluster
Better scalability provided to the world’s highest availability solution as enterprise offering
Max. number of TFO groups will be limited according to max number of CA ports/RA ports (the CA port can not be member of multiple TFO groups)
The CA ports on different CE can be assigned to same TFO group
Max. Number of TFO groups
32
Max. capacity
16PB
SAN
SAN
TFO group
© Fujitsu 2023
FUJITSU-PUBLIC

## Slide 56: Fujitsu and Veeam partnership
Virtual data protection is simplified with ETERNUS and Veeam
High data availability
Easier mgmt. of virtual backup and restore processes
Integrated storage snapshots for better efficiency
Faster disaster recovery
Drives business growth
Veeam Backup Server
Snapshots
Fujitsu ETERNUS AF/DX primary storage
Low RPO & RTO
Fujitsu ETERNUS CS800 S7
Fujitsu ETERNUS LT
VMware
VM
VM
VM
VM
FUJITSU-PUBLIC
Notes: Fujitsu Plugin:
  Offered by Fujitsu
  Separate download on the Backup & Replication download page
  Must be installed on Backup & Replication v9.5 Update 4a or newer
  It won't be included into later Backup & Replication update/version for legal reasons
  Veeam own QA department quality assurance testing for any version/update
  Official Veeam support for the plug-in
Supported Storage Systems: Fujitsu intend to support the following storage software with their plug-in: V10L86-0000 and above
  This include but is not limited to:
  ETERNUS DX Series
  ETERNUS AF Series
Supported Protocols:
  FibreChannel (Veeam Proxy needs to be physical)
  iSCSI

## Slide 57: 05 Simplified storage operations
Notes: ETERNUS SF makes it easy to get the best out of the ETERNUS Primary Storage Family. Automated Quality of Services enables you to set up a flexible tier pool. Just set the performance priority you want for each application – and that’s all you need to do! ETERNUS SF automatically monitors compliance with the settings and adjusts performance as necessary. Automated Storage Tiering (AST) refers to the ability of the storage array to move chunks of data between different disk types and RAID levels to strike the right balance between performance and space utilization, thus avoiding so-called hot spots. Frequently accessed data can be moved to high-speed drives such as SSDs, whereas data which is accessed less frequently can be shifted to cost-effective disks with large capacities. Automated Quality of Service (Automated QoS) ensures that specific applications are always allocated a predefined performance level. Adjusting the bandwidth and automatic tuning of the I/O performance makes sure that the required response time per application will be achieved. Combining both optimization features helps administrators balance performance, capacity and cost while coping with peak loads – all it takes is just a few mouse clicks!

## Slide 58: A clever combination
Non-dedup volume
Dedup volume
Pool #1
Pool #2
Auto QoS ensures business priorities
Dedup & compression reduces capacity
Guaranteed
response time
Capacity-
optimized
Balances performance & cost
Flexible configuration is a must
Switch it on volumes for capacity optimization
Keep it off for performance SLAs
Auto quality of service
Guarantees response time to every application
Keeps the noisy neighbor under control
Notes: all-flash storage for all tier one applications brings new challenges
Be aware though that data reduction technologies do not suit all data types – some are already compressed, for example.
In addition, turning on data reduction inherently adds a degree of latency back to the storage, which may be a bad idea if absolute performance is key.

## Slide 59: Eco-system

## Slide 60: Eco-system integration
PRIMERGY
Exchange Server, SQL Server, SharePoint Server, Windows Server Failover Cluster
Oracle Database/RAC, Oracle Solaris Cluster
SymfoWARE, PRIMECLUSTER
VERITAS Storage Foundation
SAP solutions (CRM, ERP…)
IBM Power Systems, IBM System x
HP ProLiant, HP Integrity
DELL PowerEdge
AIX
HP-UX
Windows Server
Oracle Solaris
VMware
SUSE Linux
Red Hat Enterprise Linux
Connectable to various servers
Supports various OS
Supports various middleware
FC16G
Ethernet 10G
iSCSI 1G/10G
ETERNUS
AF series

## Slide 61: ETERNUS AF fully integrated into VMware
ETERNUS SF Management ETERNUS AF APIs
vSphere
vCenter
ESX Storage Stack
VI Client
VM
ETERNUS AF
VMFS
VMware LVM
Datamover
NMP
SATP
VMware Multi-Pathing plug-in for ETERNUS
HBA Drivers
ETERNUS VAAI support
(former ETERNUS VAAI Plug-in)
VASA
vStorage API for Storage Awareness
ETERNUS VASA Provider
ETERNUS
vCenter Plug-in
FC/FCoE/iSCSI
ETERNUS DX features
QoS, TFO, ACM, ….
ETERNUS VVOL
vRealize Operations
ETERNUS Mgmt. Pack for VMware vRealize Operations
VMware Native Multipathing Plug-In
ETERNUS SF SRA
Storage Replication Adapter
SRM
vCenter Site Recovery Manager

## Slide 62: Other supported virtualization platforms
Functions on Windows Server 2012 Hyper-V Live Storage Migration, Hyper-V Replica, Offload Data Transfer
Supports various virtualized platforms
Hypervisors
Citrix XenServer/ Xen Desktop
Oracle VM
Egenera BladeFrame
OS-standard virtualization functions
AIX Virtual I/O Server
HP-UX InteglityVM
Linux KVM/Xen
Supports Windows Hyper-V functions
Notes: ETERNUS AF series supports major virtualized platform.

## Slide 63: Product related services

## Slide 64: Product related services
1 Service levels and offerings are subject to local market requirements
Details are available at http://www.fujitsu.com/global/products/product-support-services/
Response services
Different Service Levels1
Onsite service with defined onsite response time
  4 hours
  Next Business Day (NBD)
Service time
  9×5
  24×7
HDD retention, optional
Proactive support, optional
Warranty
Recovery services
Onsite service with defined recovery time
  4 hours
  24 hours
  NBD
Service time
  9×5
  24×7
HDD retention, optional
Proactive support, optional
Support pack
Different Service Offerings1
Has to be purchased within 90 days of the product purchase
One-time up-front payment
Service contract
Can be purchased at any time during the product lifecycle
Contract fees are paid in regular installments or as otherwise agreed
Safeguarding datacenter operations
ETERNUS AF systems are designed for highest availability and reliability.
Additionally, Fujitsu offers a variety of Product Support Services safeguarding datacenter operations.
Valid for a fixed service period of 1 to 5 years
Valid for at least 1 year
Support Packs for renewal extend the service of an existing Support Pack by a fixed period of time
Automatic renewal after the minimum service period
Notes: ETERNUS DX are designed for highest availability and reliability. However, datacenter operations should be safeguarded by Product Related Services.
Depending on local requirements Fujitsu offers a variety of Product Support Services for hardware and software. Customers can select the appropriate services according to their specific requirements. Even sophisticated services like guaranteed hardware recovery times and proactive support services are on hand in mature markets.

## Slide 65: Additional information

## Slide 66: Resources
© Fujitsu 2023
66
FUJITSU-PUBLIC
For additional information, please visit:
https://www.fujitsu.com/global/ products/computing/storage/ all-flash-hybrid.html
  Datasheets
  Analyst reports
  Brochures & flyers
  Videos
  White papers
  Case studies
  And more ...
Notes: Additional information are available in the Internet.

## Slide 67: One ETERNUS family: built for the digital world
Easy upgrades and maximum system interoperability
Guaranteed service levels with minimal performance compromise
Credibility and long history of dependable performance
Maximum data efficiency
Non-stop business continuity
Seamless family architecture
Optimized for peak performance
Intelligent data management
Always available and solidly reliable
Simplified storage operations
67
© Fujitsu 2023
FUJITSU-PUBLIC
ETERNUS DX
ETERNUS AF
Notes: This slide captures the summary of key differentiators and corresponding benefits of the ETERNUS Primary Storage Family.

## Slide 68: Thank you